## Slide 1: Decagon Devices Environmental Research Instruments
Matt Galloway
Decagon Devices, Inc.
Pullman, WA USA

## Slide 2: Where is Decagon?

## Slide 3
Washington State University, Pullman

## Slide 4
The Palouse region, Washington, USA

## Slide 6: Decagon History

## Slide 8
Now 180+ employees
Notes: 8

## Slide 9: Decagon’s Mission
Develop innovative, simple, and accurate instruments that solve problems for environmental researchers

## Slide 10
Decagon’s assets: Scientific Expertise

## Slide 11: Decagon’s Assets: 改善: Kaizen
Continual improvement: in design, manufacturing, and all processes

## Slide 12: Decagon’s Thermal and Electrical Conductivity Probe (TECP): 2007 Mars Lander
Notes: 12

## Slide 13: TECP objectives
Learn more about how heat flows in Martian regolith
  Ground-truth for plentiful remote sensing data
Determine if unfrozen water may exist under sunlit conditions in trench
  Answers: “Can liquid water occur on Mars?”
Study vapor phase water transport
  Examine how ice migrates from pole to pole
Prototype TECP probe
Notes: 13

## Slide 14: Plant Canopy Measurements

## Slide 15: AccuPAR Ceptometer model LP-80
What does the AccuPAR Measure?
PAR (Photosynthetically Active Radiation
LAI (Leaf Area Index) calculated using PAR measurements above and below the canopy, and using other variables.
Decagon invented this type of instrument in 1988 (Sunread, Sunscan, PAR-80, LP-80)

## Slide 16: What is PAR?
Acronym for Photosynthetically Active Radiation.
Defined as the light in the 400 to 700 nm range of the spectrum (visible range).
Light that is most useful to plants for photosynthesis.
Expressed by AccuPAR as mmol m-2 s-1, a measure of photon flux density
Electromagnetic Spectrum

## Slide 17: Leaf Area Index (LAI)
What is LAI?
Defined as: total leaf area per unit ground area
Indication of Canopy density, biomass
Used to monitor growth, infestation
Often used for ground-truthing Remote Sensing LAI data

## Slide 18: Calculating LAI
Above-canopy PAR
Below-canopy PAR
x (leaf distribution parameter)
Zenith angle (automatically calculated)
Fb (fraction of beam radiation)
AccuPAR calculates LAI based on equations from Goudraan, Norman, and Campbell using measured and supplied data:

## Slide 19: Comparison Studies
“Comparisons of three Leaf Area Index Meters in a Corn Canopy” by W.W. Wilhelm, K. Ruwe, M.R. Schlemmer in Crop Science 40:1179-1183 (2000)
  Shows that all three types are similar, AccuPAR/SunScan somewhat better than LAI-2000.

## Slide 20
Spectral Reflectance
Sensors (SRS)
NDVI bands: 630 nm and 800 nm center wavelengths
PRI bands: 532 nm and 570 nm center wavelengths
NIST traceable calibration stored onboard
Cosine diffusers for hemispherical measurement
36° sealed field stops for directional measurements
Dimensions: 43 x 40 x 27 mm
Epoxy-sealed sensor body – robust design
SDI-12 digital sensor
Decagon Em50 and CSI datalogger compatible
PRI
PRI
NDVI
NDVI
Hemispherical view sensors
Directional field stop sensor
Stacked SRS sensors
NDVI + PRI

## Slide 21
How to Measure NDVI and PRI
PRI
NDVI
NDVI
NDVI
PRI
Only two bands are needed to calculated NDVI or PRI.

## Slide 22
Typical canopy reflectance spectrum
Calculating NDVI
NIR
red
NDVI is calculated from measurements of percent reflectance (ρ) in the red and near-infrared (NIR) regions of the electromagnetic spectrum.
Percent reflectance is the ratio between upwelling (from the canopy) to downwelling (from the sky) radiation. Requires a measurement of both.
Red band is related to chlorophyll content (high absorption), NIR band is related to leaf cell structure (high scattering).
NDVI values range from -1 to 1.

## Slide 23
Gamon & Surfus (1999) New Phyt.
Calculating PRI
PRI (Photochemical Reflectance Index) was designed to estimate Light Use Efficiency (LUE) by detecting changes in the xanthophyll cycle
Xanthophyll pigments change rapidly in response to environmental conditions
PRI values range from -1 to 1.

## Slide 24
Measurement Considerations
Image credit: Chris Gough
Reflectance measurements require a top-down view of the canopy to measure upwelling radiance.
Up-looking sensors require unobstructed view of the sky.
Dual-view instruments (up/down) are a convenient way of measuring both incident and reflected light for calculating percent reflectance. They also account for changing sky conditions (e.g., clear vs. cloudy sky conditions).
SRS are lightweight, low power, and have a small footprint, making them easy to mount almost anywhere.
Downwelling
radiation
Upwelling radiation

## Slide 25: Leaf Porometer
Model SC-1
For measurement of stomatal conductance
Steady-state technique
Stomatal conductance is a primary indicator of plant stress under drought conditions

## Slide 26: How does it work?
A chamber with a fixed diffusion path is clamped to the leaf surface
Steady-state technique; measures vapor pressure at two locations in a fixed diffusion path
Calculates flux and gradient from the vapor pressure measurements and the known conductance of the diffusion path.
Atmosphere
Desiccant

## Slide 27: What can I do with a porometer?
Water use and water balance
  Use conductance with Fick’s law to determine crop transpiration rate
  Develop crop cultivars for dry climates/salt affected soils
Determine plant water stress in annual and perennial species
  Study effects of environmental conditions
  Schedule irrigation
Optimize herbicide uptake
Study uptake of ozone and other pollutants

## Slide 28: Case study: Washington State University wheat
Researchers using steady state porometer to create drought resistant wheat cultivars
  Evaluating physiological response to drought stress (stomatal closing)
  Selecting individuals with optimal response

## Slide 29: Case Study: Stress in wine grapes

## Slide 30: VP-4 RH/Temp/Barometric pressure Sensor
Digital sensor for use with Em50 loggers
Measures vapor pressure and temperature with a capacitance sensor and thermistor
Should be used with Decagon’s radiation shield for outdoor use

## Slide 31: RT-1 Temperature Sensor
Measures from – 40°C to 60°C
Accuracy: ±0. 5 ° from 5 to 40°C; ±1°C outside this range
Can be used in air, soil, or liquid. If used in air, a radiation shield should be used.

## Slide 32: Leaf Wetness Sensor
Determines presence and duration of leaf moisture
Capacitance technology, does not require painting or maintenance
All probes are calibrated to same dryness baseline voltage
Water condenses and evaporates from the surface at the same rate as it does on leaves

## Slide 33: Leaf Wetness applications
Disease prediction

## Slide 34: Pyranometer / PAR sensor
Manufactured by Apogee Instruments
Configured to connect to our Em50
Measures total solar radiation (W/m2), PAR sensor measures mmol/m2/s
Important for energy balance studies and micro-climate monitoring.
Comes with leveling plate

## Slide 35: ECRN-100 Rain Gauge
Resolution : 0.2 mm
Double-spoon tipping bucket

## Slide 36: DS-2 Sonic Anemometer
For micro-climate monitoring for plant studies
0-30 m/S range
0.01m/S resolution
Direction: 0-359°, ±3°

## Slide 38: Soil Water Content /Water Potential

## Slide 39: Dielectric Soil Moisture Sensors
Hi-frequency capacitance (FDR)
  -- Measures the dielectric constant of the soil
Designed to be buried in soil for long-term monitoring of soil moisture
Measurement is made by processor inside probe head

## Slide 40: Analog soil moisture sensors
10HS: 10 cm probe length, 3-15 VDC — large sample area (~1 liter)
GS1: Ruggedized sensor, 5cm steel needles, 3-15 VDC
EC-5: 5cm probe length, 2.5-3 VDC
MAS-1: 4-20 mA sensor, 5cm probe length

## Slide 41: Digital Sensors
GS3: Water content, EC (0-23 dS/m) and temperature. For soil or soil-less substrates
5TE: Water content, EC (0-23 dS/m) and temperature. For field soils only.
5TM: Water content and temperature. For field soils
All digital sensors are SDI-12 compatible

## Slide 42: Applications: Plant–water relations
Courtesy Texas A&M Horticulture

## Slide 43: Applications: Irrigation Scheduling

## Slide 44: Applications: Hydrologic monitoring

## Slide 45: Applications: Hazardous waste monitoring

## Slide 46: Applications: monitoring slope stability

## Slide 47: MPS-6 Matric Potential Sensor
For in-situ monitoring of water potential
Range: -10 to -500 kPa(pF 2 to pF 3.71)
Uses capacitance method to measure water content of a known ceramic matrix
Digital output

## Slide 48: Sensor Theory
  Measure water content of a known porous material with a pre-established SWCC, giving us matric water potential.
Matrix (Side View)
Sensor (Side View)
Confined EM Field
Metal Plate
Metal Plate
Notes: 48

## Slide 49: MPS-6 Advantages
No maintenance
Good accuracy in plant-available range
Each sensor individually calibrated at 6 points
Also measures soil temperature
Water Potential is a better indicator of plant available water than water content

## Slide 50: Em50 Data Logger
Weatherproof,-40° to 45°C measurement
5 ports
Uses 5 AA alkaline batteries, low power usage.
Programmed via RS232 cable connected to COM Port.
Measures every minute, then averages and stores readings according to how it’s programmed. It can store any interval between 1min. and 1 day.
Measures other micro-environment sensors that Decagon sells
Storage Capacity:
1MB non-volatile flash (28,672 scans on all 5 ports).

## Slide 51: Em50G: Remote logger
4G/LTE-enabled logger, delivers data via mobile network providers to Decagon’s secure server
Data is available at any internet connection

## Slide 52: How does it work?
Computer + Software
+ Internet
Em50G
Logger + Sensors
GSM/GPRS Cell Tower
Internet
Decagon
Internet Server

## Slide 54: ECHO Utility
You can:
Configure ports
Name logger
Set logging interval
Download data
Scan ports
- Does not graph
- Cannot apply calibrations in program
Free software that comes with any Em50 and Em5b purchase

## Slide 55: DataTrac

## Slide 56: Hydrology Equipment

## Slide 57: WP4C Dewpoint Water Potential Meter
Measures Water Potential of Soils, Seeds, Organic Matter, etc.directly MPa and Pf (log base 10 of MPa)
Easy to use, more robust than thermocouple psychrometers
Temp. controlled
Range: -0.05 to -300MPa

## Slide 58: Chilled-mirror Dewpoint Technique
Infrared Sensor
Optical Sensor
Mirror is chilled until dew is formed. The temperature at which saturation is achieved is determined by observing condensation on a chilled surface (mirror).
Advantages
Wide measurement range
Rapid measurement ~ 5 min.
High reliability
Low Maintenance
Sample
Mirror
Fan

## Slide 59: Moisture Release Curves

## Slide 60: pF Plot to get Soil Swelling

## Slide 61: Expansive Soil Classification from McKeen(1992)
Class | Slope | Expansion
I | > -6 | special case
II | -6 to -10 | high
III | -10 to -13 | medium
IV | -13 to -20 | low
V | < -20 | non-expansive

## Slide 62: Vapor Sorption Analyzer (VSA)
Range: -10 to -475 MPa.
Accuracy: ±1MPa or ±1%
Operating Temperature: 15 to 40°C
Auto-generated moisture release curves
Static humidity feature to watch how soil adsorbs water over time

## Slide 63: VSA data

## Slide 64: Vapor Sorption Analyzer
Static humidity feature to watch water adsorption vs. time

## Slide 65: Mini-Disk Infiltrometer
Measures Soil Hydraulic Conductivity for:
Soil Hydrology Studies
Erosion Studies
Classroom Instruction
FEATURES:
Adjustable suction rate (0.5 to 6cm)
Sintered stainless steel disk
Removable parts

## Slide 66: Dual-head Infiltrometer
For In-situ saturated hydraulic water content
Automated falling-head method, measures flux rate at a set water level and 2 pressure heads to calculate infiltration rate
Hydrologists, civil and geotech engineering
EPA/pollution monitoring
Automated!

## Slide 67: Design
Maintain constant water level at 5 cm
Capacitance water level sensor
Use air pressure to simulate different pressure heads

## Slide 68: Setup in Field
Configure test
Walk away

## Slide 69: How we use the data?
Pressure
Chart: Time, Min
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55
 | -21.573 | -12.213 | 0.657 | 4.11 | 4.037 | 3.756 | 4.097 | 4.373 | 4.316 | 4.341 | 4.295 | 4.511 | 4.508 | 4.154 | 4.597 | 10.941 | 13.967 | 14.648 | 14.734 | 14.14 | 14.661 | 14.57 | 14.339 | 14.141 | 14.74 | 14.59 | 14.424 | 14.561 | 14.735 | 14.613 | 7.977 | 4.397 | 4.064 | 4.339 | 4.152 | 4.186 | 4.517 | 4.219 | 4.241 | 3.999 | 4.522 | 4.481 | 3.875 | 3.949 | 4.367 | 10.176 | 14.666 | 14.774 | 14.014 | 14.89 | 14.884 | 14.76 | 14.663 | 14.322 | 14.214
Flux
Chart: Time, Min
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55
 | 0.0298 | 0.018705 | 0.020037 | 0.020028 | 0.020342 | 0.018542 | 0.0211 | 0.0207 | 0.02082 | 0.02066 | 0.02054 | 0.0206 | 0.02066 | 0.02054 | 0.02058 | 0.02152 | 0.02322 | 0.02484 | 0.02672 | 0.02804 | 0.02876 | 0.0286 | 0.02848 | 0.0283 | 0.029 | 0.02888 | 0.02922 | 0.02912 | 0.02916 | 0.02836 | 0.02738 | 0.0255 | 0.02406 | 0.0227 | 0.02192 | 0.02152 | 0.02166 | 0.02172 | 0.02162 | 0.02106 | 0.02106 | 0.0207 | 0.02054 | 0.02058 | 0.02092 | 0.02168 | 0.02348 | 0.02506 | 0.02692 | 0.02802 | 0.02872 | 0.02852 | 0.02846 | 0.02762 | 0.02738

## Slide 70: CTD Sensor (conductivity, temp., depth sensor)
Water Depth
Range 0 -5 or 0-10 m
Accuracy ±0.2 % of span
Resolution 1 mm from 0-5, 2mm from 5-10
Electrical Conductivity
Range 0 to 120 dS/m (mS/cm)
Accuracy ±5% of reading
Resolution 1.2% of reading
Temperature
Range -40 to + 50 °C
Accuracy ±1 °C
Resolution 0.1 °C

## Slide 71: CTD Uses
Streambeds
Piezometer wells

## Slide 72: ES-2: EC and T sensor
For monitoring EC and temperature in liquid water
Range:
Electrical Conductivity: 0 to 120 dS/m
Temperature: -40 to 50°C
Resolution:
Electrical Conductivity: 0.001 dS/m
Temperature: 0.1°C
Accuracy:
Electrical Conductivity: + 0.01 dS/m or + 10 % (whichever is greater)
Temperature: + 1°C

## Slide 73: Drain Gauge: Passive Capillary Lysimeter
Purpose: to measure deep drainage (flux and solute analysis) below the root zone
Model G3

## Slide 75: Thermal Properties

## Slide 76
Thermal Conductivity/Resistivity
Thermal Diffusivity
Specific Heat Capacity
Liquid or Solid Samples, manually or unattended measurement.
KD2 Pro
Thermal Properties Analyzer

## Slide 77: KD2 Pro Applications:
Soil heat flux for biological processes

## Slide 78: KD2 Pro Applications:
Insulation

## Slide 79: KD2 Pro Applications:
Nanofluids

## Slide 80: KD2 Pro Applications:
Petroleum products

## Slide 81: KD2 Pro Applications:
Thermal Backfill